## Slide 1: Basic Surveying
Tim Howell

## Slide 2: Surveying defined.
Land Surveying: The science and art of determining relative positions of points above, on, or beneath the surface of the earth, or establishing such points. ~Brinker and Wolfe
Forensic: belonging to, used in, or suitable to courts… ~Merriam-Webster

## Slide 3: Georgia-Tennessee Line

## Slide 4: Distances
Rod/pole/perch
Chain and links
Decimal feet or meters
  127.18’ = 127'-2 1/16“
  1 inch equals 0.08333 feet
  1/16 of an inch equals .0052 feet

## Slide 5: Horizontal, vertical, and slope…

## Slide 6: Bearings
Read as “degrees, minutes, seconds”
° = degree
‘ = minutes
“ = seconds
360 degrees in a circle
60 minutes in a degree
60 seconds in a minute

## Slide 7: Significant Digits
Distances
Pole
  ½ or ¼ = ± 4-8 feet
Chain
  ½ or ¼ = ± 16-33 feet
Foot
  Tenth = ± <1 foot
  Hundredth = ± <0.1 feet
Angles
Degree @ 100’
  ± 1.75 feet
Minute @ 100’
  ± 0.029 feet
Second @ 100’
  ± 0.0005 feet

## Slide 8: Error of Closure
Tennessee State Minimum Standards
Urban Survey – Category I = 1:10,000
Rural Survey – Category II = 1:7,500
All Others – Category III = 1:5,000
1 acre city lot with an 835'± perimeter is allowed 0.083' or 1 inch of error
10 acre rural tract with 2640' of perimeter can have 0.352' or 4 ¼ inches of error
A 500 acre tract can be easily allowed 2.5' of error.

## Slide 9: Elements of a curve
Radius
Tangent
Delta (Δ)
Chord Bearing
Chord Distance
Length (arc length)

## Slide 10: Two types of surveyors…
Mathematically inclined
Holds that dimensions on a deed supersede all others and that a surveyor isn’t there to make “legal” inferences but to document and re-establish if the variation is too great.
*Creates “pin cushion” corners.
Legally inclined
Also referred to as “fence line” surveyors.
Tend to hold field evidence over math. Believes in the hierarchy of evidence and tries to abide by it.
*Creates discrepancies between deeds and the real world.

## Slide 11: Hierarchy of Evidence
Senior Rights
Writings
Intent of Conveyances
Calls for surveys
Monuments
  Natural
  Artificial
  Record
Measurements
  Direction
  Distance
  Area

## Slide 12: Point of Beginning Traverse Traverse Points Closure

## Slide 13: Placing an order…
Corner Location
Alta Survey
Mortgage Survey
Lot or Boundary
  Marking Lines
  Topograpic
  Legal Description
Elevation Certificate
Site Plan
Development
  Subdivision
  PUD
  Condominium

## Slide 14: Things that affect costs
Topography
Ground cover
Area
Boundary
Region
Level of difficulty
Age or previous survey
Lack of previous survey
How soon is it needed?
Level of Detail
Additional Services
  Marking line
  Topograhic survey
  ALTA/ACSM
Liability

## Slide 15: What happens after you call…
Research
Reconnaissance
Measurement
Calculation
Monumentation
Drawing
Submission/Delivery

## Slide 16: Flood Definitions
FEMA
FIRM
Elevation Certificate
LOMA
Floodplain
Floodway
Special Flood Hazard Area
100-year flood
500-year flood
Base Flood Elevation
Flood Vent

## Slide 17: Waterway Cross Section

## Slide 18: FIRMette

## Slide 19: Elevation Certificate

## Slide 20: Elevation Certificate

## Slide 21: Thank you
Timothy J Howell, RLS
121 Dorothy Dr Talbott, TN 37877
865-742-2557
tim@tnlds.com
www.tnlds.com